## Slide 1: Recent Advances in the Field of Satellite Data Uncertainties
Claire Bulgin1, Chris Merchant1, Darren Ghent2
1University of Reading, UK
2University of Leicester, UK

## Slide 2: Why do we need to provide uncertainties?
All measurements (in-situ and remote sensing) have an associated uncertainty:
Every measurement we make deviates from the ‘true’ surface temperature due imperfections in the instrumentation and measurement process.
We need to understand this uncertainty in the measurement in order to use the data properly.
Error and uncertainty are two different concepts…
Error: How different is the measured value from the true value?
Uncertainty: To what degree is the measured value in doubt?
Measurement error is often unknown (and if we did know what it was we would correct for it). We therefore provide an uncertainty, a measure of the dispersion of the error distribution.

## Slide 3: How do uncertainties propagate?
Uncertainties arise at each step of the measurement process:
Uncertainties arising early in the process need to be propagated through each stage of the processing.
New uncertainties will be introduced at each stage of the processing.

## Slide 4: How do uncertainties propagate?
Uncertainties arise at each step of the measurement process:
Uncertainties arising early in the process need to be propagated through each stage of the processing.
New uncertainties will be introduced at each stage of the processing.

## Slide 5: How can we understand and quantify the uncertainties for a given processing step?
We start from the measurement equation. Lets consider first a LST retrieval in the form:
z=g(y,β)+0
y = observations β = retrieval parameters +0 = process

## Slide 6: How can we understand and quantify the uncertainties for a given processing step?
We start from the measurement equation. Lets consider first a LST retrieval in the form:
z=g(y,β)+0
y = observations β = retrieval parameters +0 = process
LST=af,i,pw+bf,i(T11-T12)n+(bf,i+cf,i)T12 + 0

## Slide 7: How can we understand and quantify the uncertainties for a given processing step?
We start from the measurement equation. Lets consider first a LST retrieval in the form:
z=g(y,β)+0
y = observations β = retrieval parameters +0 = process
LST=af,i,pw+bf,i(T11-T12)n+(bf,i+cf,i)T12 + 0
{T11, T12} {a, b, c} {+0}

## Slide 8: How to construct an uncertainty budget
Measurement Term | Normal Notation | Effect | Effects expected | Correlation length scale | Attributed uncertainties | Sensitivity
β | a | 1 | Fractional vegetation error | s | FCOVER uncertainty | 
 |  | 2 | Fitting error (atmospheric and emissivity) | s | Fitting residual | *
 |  | 3 | Precipitable water error | s | Not attributed | 
 | b | 4 |  |  |  | 
 |  | 5 |  |  |  | 
 | c | 6 |  |  |  | 
 |  | 7 |  |  |  | 

## Slide 9: The complete uncertainty budget

## Slide 10: The complete uncertainty budget
Uncertainties introduced directly in the retrieval

## Slide 11: The complete uncertainty budget
Uncertainties propagated through from the satellite measurements

## Slide 12: The complete uncertainty budget
What is included in the ‘+0’ term?

## Slide 13: The +0 Term
Measurement Term | Normal Notation | Effect | Effects expected
+0 | Geolocation | 12 | Correction of known geolocation mismatch
 |  | 13 | Re-projection of native instrument grid to image grid
 | Cloud Detection | 14 | Undetected cloud
 | RTM | 15 | Error in RTM simulation
 | NWP | 16 | Error in RTM inputs

## Slide 14: Why do we use this approach?
Starting from the measurement equation as illustrated on the previous slides has a number of benefits:
It is methodological considering each component in turn
It is rooted in metrology
It is transparent for both data users and data producers
It is a mean to identify gaps

## Slide 15: What do we provide to data users?
Our objective for uncertainty information provision is:
To provide uncertainties for every LST retrieval made.
To provide uncertainties for products at different levels (L2, L3).
To provide uncertainties for data re-gridded at different resolutions.
To derive these uncertainties independently of in-situ data.
One key benefit of deriving uncertainties independently of in-situ data is that we can then use in-situ data to validate both the retrieved LST and the associated uncertainty.

## Slide 16: What do we provide to data users?
In our data products we provide:
Total uncertainty
Three additional categories of uncertainty information:
  Uncertainties arising from random error effects (uncorrelated between observations)
  Uncertainties arising from locally systematic error effects
    For LST products there are typically two components in this category – uncertainties from surface processes and uncertainties from atmospheric processes
  Uncertainties arising from large-scale error effects
The reason for providing the breakdown of uncertainty components is to allow the uncertainties to be correctly propagated in any further processing or generation of derived products.

## Slide 17: Some Example products
MODIS TERRA LST and breakdown of uncertainties components

## Slide 18: Some example products
MODIS TERRA L3C Daily LST and total uncertainty

## Slide 19: Validation of uncertainties
Validation of uncertainties tests the goodness of fit between:
The uncertainty calculated from the difference between the satellite and in-situ measurements (σdiff)
The total satellite product uncertainty

## Slide 20: Validation of uncertainties
Validation of uncertainties tests the goodness of fit between:
The uncertainty calculated from the difference between the satellite and in-situ measurements (σdiff)
The total satellite product uncertainty
σsat = the total uncertainty in the satellite observation

## Slide 21: Validation of uncertainties
Validation of uncertainties tests the goodness of fit between:
The uncertainty calculated from the difference between the satellite and in-situ measurements (σdiff)
The total satellite product uncertainty
σsat = the total uncertainty in the satellite observation
σground = the total uncertainty in the in-situ observation

## Slide 22: Validation of uncertainties
Validation of uncertainties tests the goodness of fit between:
The uncertainty calculated from the difference between the satellite and in-situ measurements (σdiff)
The total satellite product uncertainty
σsat = the total uncertainty in the satellite observation
σground = the total uncertainty in the in-situ observation
σspace = the geophysical uncertainty associated with comparing a point measurement with an area average

## Slide 23: Validation of uncertainties
Validation of uncertainties tests the goodness of fit between:
The uncertainty calculated from the difference between the satellite and in-situ measurements (σdiff)
The total satellite product uncertainty
σsat = the total uncertainty in the satellite observation
σground = the total uncertainty in the in-situ observation
σspace = the geophysical uncertainty associated with comparing a point measurement with an area average
σtime = the geophysical uncertainty from comparing observations at different times

## Slide 24: Validation of uncertainties
Validation of uncertainties tests the goodness of fit between:
The uncertainty calculated from the difference between the satellite and in-situ measurements (σdiff)
The total satellite product uncertainty
σsat = the total uncertainty in the satellite observation
σground = the total uncertainty in the in-situ observation
σspace = the geophysical uncertainty associated with comparing a point measurement with an area average
σtime = the geophysical uncertainty from comparing observations at different times
σtime = the geophysical uncertainty due to the difference in measurement depth (MW only)

## Slide 25: Validating uncertainties
Retrieval Uncertainty
Uncertainty from satellite and in-situ differences
Expected uncertainty model:
This doesn’t tend to zero due to uncertainties in the in-situ data and data matching process

## Slide 26: Summary
In summary:
We derive our uncertainties independently of in-situ data, based on the measurement equation for the retrieval process.
We provide to the user both total uncertainty, and a breakdown of the uncertainty components by correlation length scale to enable correct propagation of these to derived products.
We validate the uncertainties in addition to the LST using in-situ observations.