## Slide 1: FREQUENCY ANALYSIS OF CLIMATE DATA
Suhyb Salama, University of Twente

## Slide 2: Learning outcomes
After completing the lecture and associate exercises you should be able to:
Differentiate between empirical and analytical statistical inferences
Differentiate between analytical techniques to analyse too little or too much water
Apply statistical inferences to analyse climatic data records on water availability
Calculate the return period and the probability of extreme events of too little and too much water

## Slide 3: Frequency
Frequency is the number of times, during a specific period, that a hydrological variable (e.g., soil moisture or rainfall) of magnitude x or lower (or higher) will occur at a location.
x is a random variable, its magnitude can not be predicted with certainty.
Discrete and continuous data.

## Slide 4: Probability
Probability 𝑃(𝑥) of 𝑥 may be described as the relative frequency with which 𝑥 occurs or will occur in the long run.
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
0.8
0.9
1
That you can go through a black hole and return
That you will get old
That you will get a baby boy

## Slide 5: Probability distribution function
, Cumulative probability distribution function

## Slide 6: Probability density function
, which is the slope of the cumulative distribution function.
This also means that is equal to the area under curve to the left of .

## Slide 7: Descriptors of probability distributions
Moments
Quantiles
Return period
Empirical probability plots
Theoretical probability distribution functions

## Slide 8: Moments
nth moment about the origin (x=0) is:
1st moment is the mean: the expected value of a random variable
2ed moment : mean square deviation
nth moment about the mean is
2ed moment : variance denoted
The coefficient of variability used to characterise the dispersion
Skewness : lack of symmetry

## Slide 9: Quantiles
Quantiles are (n-1) values that divide the probability distribution into n equal intervals of probabilities of
Median  divides the distribution function into equal parts with probability
Lower quartile
Upper quartile
For n= 100 (or multiple), quantiles are called percentiles

## Slide 10: Return period
The reciprocal of the probability that a certain value x will be exceeded is referred to as the return period or reoccurrence interval or exceedance level.
, for increase severity with magnitude: flood
, for decrease severity with magnitude: drought
Express the number of observations required until x is exceeded once.

## Slide 11: More on return period
If p is probability of success, then (1-p) is the probability of failure.
Find probability that () in N years.
And also

## Slide 12: Empirical probability plots
Graphic representation of probability of individual data in a record against their respective magnitude.
Also known as frequency plot or curve.
For a record of data consisting of n items X (e.g., rain intensity) measured at a regular interval (e.g., hourly)
Rank X (e.g., rain intensity) in decreasing order;
Assign order number m to the ranked X (i.e., 1,2,3,…..n)
Estimate the empirically probability that the magnitude of x will not be exceeded or number of times that x exceeded X_m

## Slide 13: Theoretical probabilities of extremes
Extreme values – maximum or minimum values of sets of data: e.g., annual minimum soil moisture.
When the number of selected extreme values is large, the distribution converges to one of the three forms of EV distributions called Type I, II and III.
This is called the extreme value theorem, which states that maximum of a sample of Independent and identically distributed (Iid) random variables, after proper normalisation, can only converge in distribution to one of 3 possible distributions: the Gumbel (type I), the Fréchet (type II), or the Weibull (type III).
http://www.math.wm.edu/~leemis/chart/UDR/UDR.html

## Slide 14: Types of extreme value distributions
The general form of the generalized extreme values distribution combines the three distributions Gumbel, Fréchet and Weibull (also known as type I, II and III extreme value).
Gumbel relates to largest extreme value
Frechet relates to largest extreme value
Weibull relates to smallest extreme value
Notes: We will focus on Wiebull

## Slide 15: Frequency analysis of drought with Weibull
The correct procedure is select the distribution that best describes the data
For example, the two parameters Weibull distribution has a closed analytical form and is widely employed for extreme value analysis of drought:
Based on the work of T.C. Sharma & U.S. Panu (2015) Predicting return periods of hydrological droughts using the Pearson 3 distribution: a case from rivers in the Canadian prairies, Hydrological Sciences Journal, 60:10, 1783-1796, DOI: 10.1080/02626667.2014.934824
It has the form
The return period has a closed form
Where is the drought length or magnitude scale, shape factors and is the gamma function where
is the average number of drought spells (ns) over a sampling period of T weeks or months

## Slide 16: Frequency analysis of drought with Weibull
From the data calculate the mean and standard deviation of drought events
and
Substitute these values in and to compute scale, shape factors
Estimate the return period
Be careful with the sign when you work with indices that have negative values

## Slide 17: Computing the scale and shape factors
With some algebra we can arrive to
Can you?
How to solve the first equation using spread sheet software?

## Slide 18: Computing the scale and shape factors
Use Goal Seek in
Data> What If Analysis

## Slide 19: Exercise 1: too little water
Data on soil moisture index is calculated for the Netherlands as area averaged and for the last 3 years
(sheet 1 Soil Moisture> of the excel sheet 6.1_Data4Exercises_FreqAn)
The index is computed as follows
For month 1 use ,
Where: soil moisture for month ,
, are the long-term monthly climatology mean, minimum and maximum (of a certain month over the years of observations)

## Slide 20: Exercise 1: too little water
From the data:
Estimate the return period of drought intensity of -2
Estimate the return period of drought duration of 3 and 6 months
Later we need to establish the Severity-Duration-Frequency curves of drought

## Slide 21: Back to the cause
As you remember we first will have metrological drought which is caused by shortage in precipitation and excesses in evapotranspiration
So let us analyse the rain

## Slide 22: Precipitation
Precipitation is a crucial link in the hydrologic cycle, and its spatial and temporal variations are enormous.
Precipitation is any product of the condensation of atmospheric water vapor that falls under gravity.
There are five types of precipitations: Snow, Sleet, Freezing + cold rain, Hail,
Rain Rainfall being the predominant form of precipitation causes stream flow, especially the flood flow in majority of rivers
Rain occurs in two forms: drizzles and showers:
Drizzles: last for a long period with small water droplets (<0.5 mm)
Rainfall showers: last for a short period with large (between 0.5 mm and 7 mm) an heavy water droplets
There are three causes of rainfalls: Relief rainfall, Frontal rainfall, Convection rainfall

## Slide 23: Frequency analysis of rainfall with Gumbel
Gumbel is widely employed for PDF of rainfall events causing flooding
It has the simple form
Where
,
it can be shown that , with ,

## Slide 24: Exercise 2: too much water
What you need to do
Use the sample data (sheet 2 rainfall of the Excel sheet ‘ESA CCI_Exercise on frequency analysis-dataset’)
Use an empirical plotting position approach to estimate the too much rainfall (exceedance probabilities>20mm per 30-min duration ) based on the observations.
Use Gumbel distribution to estimate the rainfall events associated with given exceedance probabilities
Later we need to establish the Intensity-Duration-Frequency curves of rainfall

## Slide 25: Exercise 2: too much water
For the first question
Rank the observations in descending order
Compute the exceedance probability associated with each rainfall volume using. Where n is the number of measurement and p is the probability of exceedance and T is the return period
Transform the volume data into rainfall intensity
Plot empirical distribution of rainfall intensity
Repeat 1-4 for each desired durations

## Slide 26: Severity – Duration – Frequency
Intensity (for rainfall) or Severity (for drought) – Duration – Frequency (I/SDF) relationships (curve): is a graph with duration plotted as abscissa, intensity severity as ordinate and a series of curves, one for each return period.
I/SDF curve gives the expected drought severity of a given duration having desired frequency of occurrence.
Return period
Intensity/ severity
Duration #1
Duration #2
Duration #3
Duration #4

## Slide 27
ESA COMMUNICATION
corporatebranding@esa.int