## Slide 1: Land Surface Temperature and NDVI for Assessing Vegetation Stress in the data-scarce Sudano-Sahelian Region of Nigeria (SSRN) An Oral Presentation at
LST_cci User Workshop 2022
Presented
by
Olapeju EKUNDAYO
University of Fort Hare,
South Africa.

## Slide 2: Introduction
Examining the Land Surface Temperature (LST) and Normalized Difference Vegetation Index (NDVI) of the Sudano-Sahelian Savannah Region of Nigeria (SSRN) is crucial to the climate and ecosystem of the region. They serve as proxy for assessing evapotranspiration, vegetation water stress, soil moisture, and thermal inertia.
The study area, SSRN, covered two different scenes of MODIS dataset: MOD13A3 monthly Terra Vegetation Index and MOD11A2 8-day Terra Land Surface Temperature imageries. The two scenes; h18/v07 and h19/v07, were downloaded, mosaicked together using the ‘Mosaic to New Raster’ Function of ArcGIS software. Subsequently, the imageries were converted to float format using the ‘Float’ function under the spatial analyst tool of the ArcGIS (since they were initially in integer form) and average to yearly spatial maps.
The Vegetation Condition Index (VCI) and Temperature Condition Index (TCI)were calculated from the downloaded MODIS LST and NDVI datasets respectively with the ArcGIS software and computed into yearly maps from year 2000 to 2010.

## Slide 3: STUDY AREA MAP
Figure 1: showing Sudan-Sahel region in Africa(on the leftside ) and Sudan-Sahel region in Nigeria (on the rightside)

## Slide 4
Yearly spatial map of Normalized Differential Vegetation Index (NDVI) and Vegetation Condition Index (VCI) are produced from MOD13A3 MODIS terra imageries to study the vegetation health and condition of the study area.
Yearly land surface temperature (LST) spatial maps are produced from MOD11A2 MODIS terra imageries of the study area from the year 2001 to 2010 to study the variation in these parameters over these years .
The study area, SSRN, covered two different scenes of MODIS dataset: MOD13A3 monthly Terra Vegetation Index and MOD11A2 8-day Terra Land Surface Temperature imageries. The two scenes; h18/v07 and h19/v07, were downloaded, mosaicked together using the ‘Mosaic to New Raster’ Function of ArcGIS software.
Subsequently, the imageries were converted to float format using the ‘Float’ function under the spatial analyst tool of the ArcGIS (since they were initially in integer form) and average to yearly spatial maps.
The Vegetation Condition Index (VCI) and Temperature Condition Index (TCI)were calculated from the downloaded MODIS LST and NDVI datasets respectively with the ArcGIS software and computed into yearly maps from year 2000 to 2010.

## Slide 5: Methods
where NIR is the near-infrared region and R is the red part of the visible light region of
the electromagnetic spectrum.
VCI= () * 100
Where NDVImax and NDVImin are maximum and minimum NDVI while NDVIi was instantaneous NDVI
TCI= (LSTmax - LSTi) / (LSTmax - LSTmin) *100
where LSTmax and LSTmin are maximum and minimum LST while LSTi was instantaneous LST

## Slide 6: RESULTS AND DISCUSSION

## Slide 7: Figure 2: Spatial maps of VCI andTCI for year 2000 -2003

## Slide 8: Figure 3: Spatial maps of VCI and TCI for year 2004-2007

## Slide 9: Figure 4: Spatial maps of VCI and TCI for year 2008-2010

## Slide 10
VCI close to 50% means fair condition. Below 50% means below normal, below 35% is extreme drought.
TCI close to 50% means fair condition. Below 50% means below normal, 0% means very hot.

## Slide 11
Table 1: VCI ranges for the Sudano-Sahelian Savanna Region and the area covered by the ranges for each year in square kilometers

## Slide 12
Table 2: TCI ranges for the Sudano-Sahelian Savanna Region and the area covered by the ranges for each year in square kilometers

## Slide 13
Total Area of stressed Vegetation |  | 
YEAR | VCI (0-40%) | TCI (0-40%)
2000 | 15478.62 | 288122.73
2001 | 10860.02 | 285624.91
2002 | 13990.59 | 287778.37
2003 | 6977.26 | 287309.59
2004 | 7396.28 | 287994.75
2005 | 4403.08 | 287771.47
2006 | 2640.3 | 287957.8
2007 | 3055.88 | 286878.79
2008 | 3425.1 | 286289.14
2009 | 5850.74 | 287732.91
2010 | 2908.2 | 287330.14
Table 3: Comparison of VCI (0-40%) and TCI (0-40%) for the Vegetation Condition of the Sudano-Sahelian region of Nigeria (SSRN)

## Slide 14: Figure 5: LST time series graph for SSRN region from Feb.2000-Dec.2010
Chart: Land Surface Temperature, LST, (in degrees Celsius )

## Slide 15: Figure 6: NDVI time series graph for SSRN from Feb.2000-Dec.2010
Chart: Months

## Slide 16: Figure 7: Graph of yearly mean LST against monthly mean NDVI for SSRN from Feb.2000-Dec.2010
Chart: NDVI

## Slide 17: Figure 8: Graph showing yearly VCI variation for SSRN from 2000-2010
Chart: YEAR
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
 | 49.6388 | 50.8551 | 50.0124 | 51.9487 | 51.6762 | 52.831 | 53.8635 | 53.3555 | 53.3904 | 53.0954 | 55.1706

## Slide 18: Figure 9: Graph showing yearly TCI variation for SSRN region from 2000-2010 (linear relationship)
Chart: YEARS
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
 | 11.7369 | 15.9547 | 10.0177 | 10.9476 | 8.3131 | 14.0882 | 8.1854 | 17.179 | 11.3708 | 13.2463 | 16.2097

## Slide 19: Conclusion
The According to VCI, there was less than fair (that is, below normal) vegetation condition in years 2000, 2001 and 2002.
This suggests that the stress on vegetation due to photosynthesis and soil moisture content in the region is less throughout the period of study except for the above 3 years because there are more high values of VCI than low values throughout the period.
On the other hand, from TCI result, there was below normal vegetation condition throughout all the years. It was observed that TCI had more area covered within its lower range from 0 to 40% than the VCI.
The prevalence of low TCI values in the region depicted that the stress on the vegetation in the region is majorly as a result dryness of the soil and high land surface temperature.
The fact that a large extent of the Sudano-Sahelian region is dominantly semi-desert and steppe, could be a reason for this, as it is expected that there would be less photosynthetic activities in the region due to less dense vegetation.

## Slide 20: Some References
Abaje, I. B., Ati, O. F., Iguisi, E. O., and Jidauna, G. (2013). Droughts in the sudano-sahelian ecological zone of Nigeria: implications for agriculture and water resources development. Global Journal of Human-Social Science Research, 13(2).
Anyamba, A. and Tucker, C.J. (2005) Analysis of Sahelian vegetation dynamics using NOAA-AVHRR NDVI data from 1981–2003. Journal of Arid Environments 63, 596–614
Ayuba, H.K., Maryah, U.M. and Gwary, D.M. (2007). Climate Change Impact on Plant Species Composition in Six Semi-Arid Rangelands of Northeastern Nigeria. The Nigerian Geographical Journal, 5 (1), 35-42.
Huete, A., Didan, K., Miura, T., Rodriguez, E. P., Gao, X. and Ferreira, L. G. (2002). Overview of the radiometric and biophysical performance of the MODIS vegetation indices. Remote sensing of environment, 83(1), 195-213.
Kogan, F.N., (1995) Application of vegetation index and brightness temperature for drought detection. Advances in Space Research, 15(11):91–100.
Kogan, F. N. (1997). "Global Drought Watch from Space." Bulletin of the American Meteorological Society 621-636
Tucker, C.J. (1979). Red and Photographic Infrared Linear Combinations for Monitoring Vegetation. Remote Sensing of Environment, 8(2), 127-150.

## Slide 21: THANK YOU FOR YOUR RAPT ATTENTION