## Slide 1: Fire_cci phase 2 progress. Interactions with other ECVs
Phase 2 of the Climate Change Initiative Fire_cci project
Emilio Chuvieco
University of Alcalá

## Slide 2: Context
Fire
effects
Loss of lives and
properties
Greenhouse gas
emissions
Vegetation
succession
Run-off alteration
Soil erosion
Fire
uses
Deforestation
Grazing
Arson
Shifting
agriculture
Cyclical
Fire factors
Land
use changes
Fire policy:
suppression
Climate
changes
Population
dynamics
Increase
Decrease

## Slide 3: Fire factors: It needs biomass and dryness
Harrison, S. P., J. R. Marlon y P. J. Bartlein (2010): Fire in the Earth System, en Changing Climates, Earth Systems and Society (editado por J. Dodson). Springer Netherlands: 21-48.

## Slide 4: Fire impacts
Source: Ward et al., 2012

## Slide 5: Annual mean fire emissions 1997-2008 (GFED v3)
Global fire emissions: ~2.3 Pg C/yr
~ 1/4 of total occurs at the deforestation frontier
Van der Werf et al., 2010
g C m-2 yr-1

## Slide 6: Impacts of fire on vegetation composition
Without fire C4 PFT will increase from 27% to 56% while reducing C3.
Bond, et al. 2005

## Slide 7: Effects on human lives and properties

## Slide 8: Australia, 2009
MODIS Images: visibleearth.nasa.gov
173 people died and 7,562 people were displaced. Over 3,500 structures destroyed
450,000 ha were burned

## Slide 9: Russia, 2010
MERIS images. August, 2010 Courtesy DLR
50 people were killed. Over 2,500 houses in 150 villages and towns were destroyed
6 m ha burned

## Slide 10: Indonesia, 2015
http://fires.globalforestwatch.org

## Slide 11: Uses of BA information
GCOS:
  Estimation of emissions of trace gases and aerosols from vegetation fires.
  Provision of inputs to climate and carbon-cycle models
  Parameterization of climate-driven models for simulating BA.
Other potential benefits:
  Civil-protection: fire risk assessment.
  Ecological impacts: Soil erosion, hydrological cycle

## Slide 12: Challenges for global burned area detection
Different BA conditions:
  Different land covers.
  Different proportions burned.
  Different combustion completeness.
Sensor suitability.
Consistency of the time series:
  Different sensors / calibration issues.

## Slide 13: Fire CCI BA products
Pixel product:
  3 variables: date of detection, uncertainty, and burned land cover.
  Monthly files, continental tiles, GeoTiff format.
Grid product:
  22 variables: total burned area, standard error, % observed area, number of patches and burned area of each land cover.
  15-day files at 0.25 x 0.25 degree.
  NetCDF4 format.

## Slide 14: New tile distribution
Geotiff format, multilayer file

## Slide 15: California BA @ 300m, June 2008

## Slide 16: Central Asia BA @ 300m, June 2008

## Slide 17: Day of the Year of BA detection MERIS (2008) v3

## Slide 18: Uncertainty characterization: Monthly confidence level (%)

## Slide 19: Grid product: total yearly BA
MERIS fire_cci estimation
3.5-3.7 million km2
(Chuvieco et al., 2016, GCB)

## Slide 20: Standard error from (2008/06/22)
Burned Area

## Slide 21: Number of patches from (2008/06/22)
Burned Area

## Slide 22: Land cover from (2008/06/22)
Burned Area

## Slide 23: Validation
242 pairs of Landsat TM/ETM+ images.
130 sites for spatial validation from 2008 (red)
112 pairs for temporal validation (blue).

## Slide 24: Intercomparison: total burned area
Burned Area Sq km

## Slide 25: Differences with GFED4
Chuvieco et al., 2016, GEB

## Slide 26: Regional differences
Chuvieco et al., 2016, GEB

## Slide 27: Fire patch analysis
Chuvieco et al., 2016, GEB

## Slide 28: Gas emissions: Bottom-up approach
Emission
BA
(Burned Area)
CC
(Combustion Completenes)
EF
(Emission Factor)
ESA fire_cci
fase 1 &2
Fuel
Loads
ESA fire_cci Fase 2
DVM
Lab Measurements

## Slide 29: Mean annual CO2 emissions (GgC yr-1)
(a) GFED3.1 emission dataset, emissions from the GFED3.1 data; (b) ORCHIDEE - prognostic, emissions by ORCHIDEE prognostic simulation; (c) ORCHIDEE - GFED3.1, ORCHIDEE simulation with BA being forced by GFED3.1 burned area data; (d) ORCHIDEE - MERIS, ORCHIDEE simulation with BA being forced by ESA MERIS burned area product Chao et al., 2014

## Slide 30: Emission comparisons
 | Burned area (Mha yr-1) | CO emissions (TgCO yr-1) | Carbon emissions (PgC yr-1)
GFED4 data set | 346 | 258 | 1.6
ORCHIDEE – GFED4 | 346 | 329 | 2.0
ORCHIDEE – Prognostic | 232 | 346 | 2.0
ORCHIDEE – Fire_cci | 369 | 351 | 2.1
ORCHIDEE – Fire_cci - HIGH | 528 | 470 | 2.9
ORCHIDEE - Fire_cci - LOW | 206 | 219 | 1.3
GFED3.1 data set | 346 | 334 | 1.9
Chuvieco et al., 2016, GEB

## Slide 31: Seasonal trends in carbon emissions
Chuvieco et al., 2016, GEB

## Slide 32: Product Downloads (v3.0)
63 researchers from 26 countries (+ESA, JRC, FAO)
DGVM, fire risk, fire behavior, emissions, terrestrial ecology, fire ecology, fire management

## Slide 33: Phase 2 Processing status
Processing the Fire_cci product over the full temporal coverage of MERIS:
  Adaptation and improvements on the MERIS BA algorithm.
  Implementation at BC.
  Global processing (2003-2012).
Next tasks:
  Complete temporal series with MODIS, S-3 (2000-2016). Potential extension to 1980 (AVHRR option): LTDR.
  Small-fire database from Sentinel-2 & Prova-V (Africa).

## Slide 34: ¡Thank you!
emilio.chuvieco@uah.es http://www.esa-fire-cci.org/